# MULTIPLE LINE

# FRAME

for tufting of mattresses in multiple lines

Working procedure: The mattress is placed in a frame between one or two HECTOR Long (100cm) machines, placed opposite each other. The operator starts the process with a button and the mattress is fed into position and the tufting takes place automatically. When the pattern is finished the mattress returns to the operator.

The distance between the HECTOR machines is automatically controlled by a unique positioning system which makes it possible to program any distance and number of tufts per row. The computer can store several different patterns for different mattresses. Each tufting point can be positioned to compensate for the shrinking of the cushion, caused by the tufting process. Normal capacity is 8 tufts per sewing head and minute. The total capacity is depending on the tufting pattern and the number of stitches.

Standard equipment: 	Conveyor 2pcs 2,4mx1,8 m with supergrip band

Thread guard for the upper thread.

MULTIPLE LINE - THE MOST PRODUCTIVE AND

LABOUR SAVING WAY OF TUFTING